## Slide 2: ETHANOL DEMAND AND PRICE TREND (Highest ethanol price)
Sr. No. | YEAR | DEMAND BY OMCs Million Liters | ETHANOL PRICE, Rs./Lit | 
 |  |  | Basic | Landed
1 | 2004-05 |  | 18.0 | NA
2 | 2010-11 | 1016.6 | 27.0 | 31.82
3 | 2011-12 | 1036.5 | 27.0 | 31.82
4 | 1012-13 | 1404.1 | 27.0 | 31.82
5 | 2013-14 | 1332.5 | 41.0 | 49.50
6 | 2014-15 | 1559.4* | 41.0 | 49.50
7 | 1015-16 | 2656.3# | 42.0/45.37 (ED) | 49.50
8 | 2016-17 | 2808.9# | 39.0 | 46.95
9 | 2017-18 | 3136.0# | 40.85 | 48.69
10 | 2018-19 | 3292.6# DFPD guidelines of 18-09-2018 | 59.13 (SJ)/ 52.43 (BH & Partial SJ) / 43.46 (C)/47.13 (DG) | ???
# Requirement for 10 % Blending * Includes requirement for up to 10% blending in Six States.

## Slide 3
AGENDA
Indian Sugar surplus Vs Global sugar surplus.
BH Molasses route advantages.
Partial Sugarcane Juice route .
BH molasses route Vs Partial Sugarcane Juice route .
Sugar recovery formula.
Enhanced capacity of distilleries with BH molasses and SJ.
Choice of sugarcane processing routes for ethanol production under Indian conditions.
Conclusions.

## Slide 4: INDIAN SUGAR BALANCE SHEET 2018-19
S. N. | Particulars | Million Tonnes
1 | Opening Balance (on 1st Oct, 2018) | 10.264
2 | Estimated Sugar Production | 30.070
3 | Estimated imports | 0.000
4 | Sugar availability during the season | 40.334
5 | Estimated Sugar Sales | 26.000
6 | Exports under MIEQ | 1.000
7 | Total Estimated Off take | 27.000
8 | Closing Balance (30th Sept, 2019) | 13.334

## Slide 5
WORLD SUGAR BALANCE
Global sugar surplus of 2.64 Million tonnes in 2018-19 is forecasted as compared to previous surplus of 19.60 Million tonnes in 2017-18.
As a result, world raw sugar prices will still remain depressed.
This surplus is mainly due to soaring sugar production in India followed by Thailand and EU.
This year about 0.5 Million tonnes of sugar is expected to get diverted to ethanol production (150 Million Liters) through B Heavy molasses.
Indian surplus will still be about 12.834 Million tonnes by end of Sept, 2019.
However, global sugar deficit of 1.3 Million tonnes is also forecasted for 2019/20. Surprisingly, this swing back to deficit is coming after only two surplus seasons.

## Slide 6: USE OF BH MOLASSES IN EXISITING DISTILLERIES
BH molasses fermentation can be carried out exactly in the same way as with C molasses with same fermenters and equipment.
Temperature during fermentation should be properly controlled as fermentation rate will increase.
Heat load is going to increase if there is going to be increase in daily capacity utilization.
Distillation to be carried out using the same distillation set-up.
However, since higher alcohol concentration (12 to 13 % v/v) is targeted, distillation need to be carried-out carefully avoiding spent wash and vent losses.
High alcohol tolerant yeast should be used preferably in fed-batch fermentation system.
For achieving ZLD, same downstream effluent treatment system can be used.
In fact, COD of spent wash and total COD load is expected to get slightly reduced.

## Slide 7: COMPARATIVE ADVANTAGES OF BH MOLASSES ROUTE IN EXISTING DISTILLERY
Sr. No. | Particulars | BH molasses route | C molasses route
1. | Distillery capacity, KLPD-RS | 100 | 70
2. | Final ethanol concentration in fermented broth, % v/v | 12.5 to 13.0 | 9.0 to 9.5
3. | Final residual sugars in fermented broth, % w/v | 0.8 to 0.9 | 1.2 to 1.4
4. | Fermentation efficiency, % | 90-91 | 88-89
5. | Raw spent wash generation, Lit/Lit of ethanol | 7.0 to 7.5 | 9.3 to 9.5
6. | Raw spent wash COD, ppm | 85,000 | 110,000
7. | Concentrated spent wash generation (after evaporation), Lit/Lit of ethanol | 4.5 | 6.5
8. | Steam consumption, Kg/Lit of ethanol | 1.75 | 2.40
9. | Reduction in TRO consumption, Lit/day | 75 | 150

## Slide 8: COMPARATIVE ADVANTAGES OF BH MOLASSES ROUTE IN SUGAR MILL AND COGENERATION UNIT
Sr. No. | Particulars | BH molasses route | Final molasses route
1. | Crushing capacity, TCD | 5300 | 5000
2. | Recovery, % | 10.72 (-1.36) | 12.08
3. | Net exportable power due to electricity saving in sugar mill operation, units/day | 3,68,400 | 3,60,000
4. | Steam consumption in sugar mill operation, MT/day | 2064 | 2160
5. | ICUMSA colour of sugar, IU units | 130 | 145

## Slide 9: B-HEAVY MOLASSES ADVANTAGES
Switch over from (C) final molasses to BH molasses is fast.
Increase in distillery capacity (70 KLPD 100KLPD)
Production of BH molasses will reduce steam consumption in sugar mill and distillery that will result in bagasse saving.
Sugar colour and size can be improved.
Increased export of power from cogeneration unit.
Saving in PP/gunny bags because of reduced sugar production.
Reduction in interest burden on sugar stock with sugar mill.
Reduction in transport cost of purchased molasses.
Saving in working days of sugar mill because of additional crushing capacity.
Reduction in per liter effluent treatment cost in distillery.

## Slide 10: USE OF PARTIAL SJ IN EXISITING MILLS WITH ATTACHED DISTILLERIES
In existing sugar mills with attached distillery, partial SJ can be used either in the form of concentrated clear juice (about 250 brix, before second body) or in the form of syrup.
Required quantity of concentrated juice (250Brix) matching to the capacity of the attached distillery can be withdrawn.
The concentrated hot juice need to be cooled (on line) and taken directly to fermentation without intermediate storage.
Concentrated Juice is rich fermentation media and susceptible for contamination. Therefore, care has to be taken to avoid contamination at all stages.
OR Required quantity of syrup (550Brix) matching to the capacity of the attached distillery can be withdrawn, cooled on line and taken for fermentation by diluting with recycled spent wash.
Partial SJ will also provide some direct and indirect benefits as mentioned for BH molasses but the rate of ethanol from this partial withdrawal will be Rs. 52.43 per liter and not Rs. 59.13 per liter .
SJ route will require additional investment for PHEs, pumps, piping, valves, mass flow meters and other instruments.
Spentwash generated from SJ route will not be useful for incineration boilers.

## Slide 11: Comparison between partial SJ and BH Molasses routes
S. N. | Particulars | Unit | Sugar cane Juice | B-Heavy Molasses
1 | Distillery capacity | KLPD | 60.0 | 60.0
2 | Sugar mill capacity | TCD | 4500 | 4500
4 | Recovery of Ethanol | Lits./MT | 73.50 | 300.0
5 | Sugar cane required for ethanol production | TPD | 816.33 | NA
6 | Sugar recovery (10.5 %) | % | 8.59 | 9.00
7 | Sugar loss during ethanol production | Qtls. | 857.14 | 675.0
8 | Sugar selling price | Rs./Kg | 30.0 | 30.0
9 | Sugar loss revenue during ethanol production | Rs. Lakh | 25.71 | 20.25
10 | Cane available for sugar production | TPD | 3683.67 | 4500.00
11 | Molasses production/MT of sugar cane | % | 4.25 | 6.25
12 | Molasses production | TPD | 156.56 | 281.25
13 | Ethanol production from sugar cane juice | Lits./day | 60000 | NA

## Slide 12: REVENUE GENERATION FROM partial SJ and BH Molasses routes
14 | Ethanol recovery from C-Molasses | Lits./MT of C-Molasses | 255.00 | NA
15 | Ethanol Production from C -Molasses | Lits./day | 39922 | NA
16 | Ethanol Production from B-Heavy Molasses | Lits./day | NA | 84375
17 | Total ethanol production from sugar cane & C- Molasses | Lits. | 99922 | NA
18 | Ethanol selling price from sugar cane juice | Rs./Lit. | 52.43 | 52.43
19 | Ethanol selling price from C-Molasses | Rs./Lit. | 43.46 | NA
20 | Ethanol revenue from sugar cane juice | Rs. Lakh | 31.46 | NA
21 | Ethanol revenue from C-Molasses | Rs. Lakh | 17.35 | NA
22 | Ethanol revenue from B- Heavy Molasses | Rs. Lakh | NA | 44.24
23 | Total revenue from ethanol | Rs. Lakh | 48.81 | NA
24 | Net revenue obtained after deducting sugar loss | Rs. Lakh | 23.09 | 23.99
 |  |  |  | 0.89

## Slide 13: RAW MATERIAL PRICE IN SJ and BH Molasses routes
1 | Assumed C-molasses production in normal route | TPD | NA | 191.25
2 | Assumed C-molasses price | Rs./MT | 4000 | 4000
3 | Assumed cost of C-molasses | Rs. Lac | NA | 7.65
4 | Therefore, total B-Heavy molasses cost | Rs. Lac | NA | 27.90
5 | Therefore, per MT of B-Heavy molasses price | Rs. Lac | NA | 9920.00
6 | FRP of sugar cane | Rs./MT | 2887.50 | 2887.50
7 | Raw material cost-Sugar cane juice | Rs./Lit. | 39.29 | NA
8 | Raw material cost-C- molasses | Rs./Lit. | 15.69 | NA
9 | Raw material cost-B-Heavy molasses | Rs./Lit. | NA | 33.07
10 | Sugar loss-cost as raw material | Rs./Lit. | NA | 24.00
11 | Therefore, molasses cost as raw material in B-Heavy molasses route | Rs./Lit. | NA | 9.07

## Slide 14
NET PROFIT IN SJ and BH Molasses routes
1 | Conversion cost | Rs./Lit. | 10.00 | 10.00
2 | Cost of production in C-molasses route | Rs./Lit. | 25.69 | NA
3 | Cost of production in Sugar cane juice route | Rs./Lit. | 49.29 | NA
4 | Cost of production in B-Heavy molasses route | Rs./Lit. | NA | 43.07
5 | Total cost of ethanol production through C-molasses | Rs. Lac | 10.25 | NA
6 | Total cost of ethanol production through sugar cane juice /BH | Rs. Lac | 29.57 | 36.34
7 | Total cost of ethanol production in sugar cane juice route (SJ+C) | Rs. Lac | 39.83 | NA
8 | Net profit from ethanol production | Rs. Lac | 8.98 | 7.90
9 | Revenue lost due to sugar loss | Rs. Lac | 5.46 | NA
10 | Net profit from 4500 TCD crushing in ethanol production | Rs. Lac | 3.52 | 7.90

## Slide 15: REVISED FORMULA FOR CALCULATION OF SUGAR RECOVERY IN SUGAR MILLS USING SJ OR BH MOLASSES
In the latest revised guidelines the following formula is provided by DFPD to calculate the estimated sugar recovery had it been the conventional process based on mixed juice Purity and Pol,
Calculating sugar recovery by above given formula will result in higher recovery than the actual recovery and thus, mills will be required to pay higher FRP.
To calculate the estimated sugar recovery had it been the conventional process; the following formula can give correct results,
Where, S = Sugar Purity, J = Clear Juice Purity and M = Final Molasses Purity

## Slide 16: ENHANCED DISTILLERY CAPACITY AND POLLUTION LOAD
With use of cleaner substrate such as BH molasses or SJ, the alcohol % in wash will definitely increase which will result in increasing the production capacity of the distillery by about 1.5 times.
At the same time, the pollution load on downstream effluent treatment system is going to get reduced.
Therefore, CPCB/PCBs should allow the distilleries to run at enhanced capacity using such (BH molasses or SJ) clean substrates.

## Slide 17: CHOICE OF ROUTES UNDER INDIAN CONDITIONS
CONVENTIONAL
B HEAVY MOLASSES
Secondary Juice + B Heavy Molasses
Secondary Juice
WCJ
DRIVING
FACTORS
INCREASED ETHANOL
DEMAND
HIGHER ETHANOL PRICE
LOWER SUGAR PRICE

## Slide 18: CONCLUSIONS
BH molasses route seems to be preferred route for sugar mills with attached distilleries under prevailing rates offered by OMCs. It can result in increasing ethanol production in the country and at the same time can reduce the increasing sugar stocks.
Typically distillery capacities in the country are smaller than sugar mill capacities. Therefore, going exclusively for SJ to ethanol is not viable.
It would be difficult for Indian sugar mills to go for partial SJ to ethanol route.
There can be some variation from case to case depending on configuration of sugar mill, distillery and cogeneration units.
Indian sugar mills need to develop flexible approach to shift from sugar to ethanol or vice-versa as per the market demand.
Payment of ethanol is made within 21 days by OMCs whereas sugar sale is dependent on market conditions and invites interest burden during storage.
BH molasses brix should be maintained at minimum 860Brix and it should be cooled to 400C before going to storage tank.
A long term ethanol policy with assured prices (in relation to FRP of sugarcane) should be formulated and announced.

## Slide 19
Visit us at: www.vsisugar.com