## Slide 1
Experiences with B- heavy molasses Diversion for Ethanol Production
By
Narendra Mohan, D. Swain & Seema Paroha
National Sugar Institute, Kanpur, U.P., India
Email : nsikanpur@nic.in, director.nsi@gov.in

## Slide 2: Background
Ethanol Blending Petrol Programme (EBP) was launched by the Government in 2003 on pilot basis in some states.
Subsequently extended to the Notified 21 States and 4 Union-Territories to promote the use of alternative and environment friendly fuels.
This intervention also seeks to reduce import dependence for energy requirements and give boost to agriculture sector.

## Slide 3: Background Continued
Government has notified the National Biofuel Policy according to which 10% blending of ethanol into petrol has been targeted through various feed stocks other than the conventional route of Final Molasses.
The government initiatives and policies have significantly improved the supply of ethanol during the past four years.
The ethanol procured by Public Sector OMCs has increased from 38 crore litre in ethanol supply year 2013-14 to little above 160 crore litre in 2017-18 and this year it is expected to achieve blending to the extent of 8%.

## Slide 4: Background Continued
Consistent surplus of sugar production is depressing sugar price.
Consequently, sugarcane farmer's dues have increased due to lower capability of sugar industry to pay the farmers.
With a view to limit sugar production in the Country, Government has taken multiple steps including allowing diversion of B heavy molasses / sugarcane juice for production of ethanol.

## Slide 5: Background Continued
For many reasons including energy security, having green & renewable energy and balancing demand-supply scenario of sugar, ethanol production is being favored.
To enhance the ethanol production, the Government of India has announced a differential pricing policy for ethanol produced from conventional route, through diversion of B Heavy molasses and also through partial or 100% diversion of sugarcane juice.
It is worth noting that as compared to ethanol derived from C- heavy molasses route, diversion of B heavy molasses reduces the sugar by 15-20 % and increases ethanol availability by about 90-100%. On the other hand, diversion of sugarcane juice reduces sugar by 100% and increases ethanol availability by about 580-600%.

## Slide 6: Background Continued
The ex-mill price of ethanol derived out of B heavy molasses / partial sugarcane juice has been fixed as Rs.52.43 per litre.
The ex-mill price of ethanol derived from 100% sugarcane juice has been fixed as Rs.59.13 per litre for those mills who will divert 100% sugarcane juice for production of ethanol thereby not producing any sugar.
Additionally, GST and transportation charges will also be payable.
OMCs have been advised to fix realistic transportation charges so that long distance transportation of ethanol is not disincentivised.
OMCs are advised to prioritize ethanol in the following order 1) 100 % sugarcane juice, 2) B heavy molasses / partial sugarcane juice, 3) C heavy molasses and 4) Damaged Food grains/other sources.

## Slide 7: Expected Impacts
The decision will serve multiple purposes of reducing excess sugar in the country, increasing liquidity with the sugar mills for settling cane farmer's dues and making higher ethanol available for Ethanol Blended Petrol (EBP) Programme.
All distilleries will be able to take benefit of the scheme and large number of them are expected to supply ethanol for the EBP programme. Remunerative price to ethanol suppliers will help in reduction of cane farmer's arrears, in the process contributing to minimizing difficulty of sugarcane farmers.
Ethanol availability for EBP Programme is expected to increase significantly due to higher price being offered for procurement of ethanol from B heavy molasses / partial sugarcane juice and 100% sugarcane juice for first time.
Increased ethanol blending in petrol has many benefits including reduction in import dependency, support to agricultural sector, more environmental friendly fuel, lesser pollution and additional income to farmers.

## Slide 8: ECONOMICS OF ETHANOL PRODUCTION THROUGH DIFFERENT ROUTES
Based on the latest price of ethanol as
Rs. 43.46 from Final Molasses
Rs. 52.43 from B-Heavy Molasses
Rs. 59.13 from Direct Cane Juice
Economy of Ethanol Production has been worked out

## Slide 9: Theoretical Economics of B- Heavy Molasses Diversion Basis
BASIS
Average recovery of sugar production : 10.80
Final Molasses % Cane : 4.5
B Heavy Molasses % Cane : 6.7
Percentage Reduction of Sugar in case of B Heavy diversion : 15.73
Yield of Ethanol from Final Molasses in litre/Ton : 235
Yield of Ethanol from B Heavy Molasses in litre/Ton : 310

## Slide 10: Basis Continued
Specific Gravity of Alcohol : 0.789
Un-Fermentable Sugar % in Final Molasses : 5
Fermentation Efficiency % : 91
Distillation Efficiency % : 98
Cane Price :Rs. 297/Qtl
In order to fix the percentage of B Heavy and the recovery after B Heavy diversion, it is assumed that whatever additional ethanol that has been produced, it is at the expense of the recovery.

## Slide 11: B Heavy Diversion Route Contd….
Particulars | Units | F M | BH | 
Cane Crushed | Ton | 1 | 1 | 
Recovery | % Cane | 10.8 | 9.10 | 15.7
Sugar Price | Rs. / kg | 32 | 32 | 
Gross Revenue from Sugar | Rs. | 3456 | 2912.4 | 
Conversion cost | Rs. / kg | 5 | 5 | 
Net Revenue from Sugar | Rs. | -54 | -512.69 | 
Molasses | % Cane | 4.5 | 6.7 | 49
Ethanol Production Rate | Litre/Ton | 235 | 310 | 
Ethanol Production | Litre | 10.58 | 20.77 | 96

## Slide 12: B Heavy Diversion Route Contd….
Ethanol Price | Rs. / Litre | 43.46 | 52.43 | 
Gross Revenue from Ethanol | Rs. | 459.59 | 1088.97 | 
Conversion cost | Rs. / Litre | 12 | 12 | 
Net Revenue from Ethanol | Rs. | 332.69 | 839.73 | 
Additional Power Export | kWh | 90.00 | 92.00 | 
Power Price | Rs/kWh | 5.00 | 5.00 | 
Gross Revenue from Power | Rs | 450.00 | 460.00 | 
Conversion cost | Rs/kWh | 1.50 | 1.50 | 
Net Revenue from Power | Rs. | 315.00 | 322.00 | 
Press Mud Production | Ton | 0.035 | 0.035 | 
Price of Press Mud | Rs/Ton | 250.00 | 250.00 | 
Net Revenue from PM | Rs | 8.75 | 8.75 | 
Total Net Revenue | Rs. | 602.44 | 657.79 | 
Difference | Rs. |  | 55.35 | 

## Slide 13: B Heavy Diversion Route Contd….
Chart: Final Molasses Vs B-Heavy
| 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43
Final Molasses | 4374.3395 | 4482.3395 | 4590.3395 | 4698.3395 | 4806.3395 | 4914.3395 | 5022.3395 | 5130.3395 | 5238.3395 | 5346.3395 | 5454.3395 | 5562.3395
B Heavy | 4450.0145 | 4528.2145 | 4619.2145 | 4710.2145 | 4801.2145 | 4892.2145 | 4983.2145 | 5074.2145 | 5165.2145 | 5256.2145 | 5347.2145 | 5438.2145

## Slide 14: B Heavy Diversion Route Contd….
Chart: Sugar Price per kg
| 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43
Total Revenue | 75.675 | 45.875 | 28.875 | 11.875 | -5.125 | -22.125 | -39.125 | -56.125 | -73.125 | -90.125 | -107.125 | -124.125
Net Earnings | 40.775 | 12.975 | -4.025 | -21.025 | -38.025 | -55.025 | -72.025 | -89.025 | -106.025 | -123.025 | -140.025 | -157.025
Ethanol Price/Sugar Price | 1.6384 | 1.5888 | 1.5421 | 1.498 | 1.4564 | 1.417 | 1.3797 | 1.3444 | 1.3108 | 1.2788 | 1.2483 | 1.2193
The net profit of the plant as a whole remains positive till the price of sugar reaches between Rs. 33 and 34 per kg.

## Slide 15: Basis of comparison
Particulars | Unit | Value | 
 |  | Dhampur | Ninainadevi
Actual Average Sugar Recovery | % Cane | 10.63 | 12.24
Calculated Sugar Recovery | % Cane | 12.14 | 13.19
Loss of Recovery | % Cane | 1.51 | 0.95
B Heavy % on Cane | % Cane | 5.81 | 4.23
Alcohol Yield from B- Heavy | Liter/Ton | 310 | 317

## Slide 16: Case Study: Economics of B-Hy Diversion (DHAMPUR)
Chart: Sugar Price per kg in Rs.
| 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41
MARGIN | 39.145 | 22.5602 | 7.4602 | -7.6398 | -22.7398 | -37.8398 | -52.9398 | -68.0398 | -83.1398 | -98.2398
RATIO | 1.6384 | 1.5888 | 1.5421 | 1.498 | 1.4564 | 1.417 | 1.3797 | 1.3444 | 1.3108 | 1.2788

## Slide 17: Case Study: Economics of B-Hy Diversion (NINAIDEVI)
Chart: Margin in case of B-Heavy NINAIDEVI
| 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41
MARGIN | 41.1453 | 31.5429 | 22.0429 | 12.5429 | 3.0429 | -6.4571 | -15.9571 | -25.4571 | -34.9571 | -44.4571
RATIO | 1.6384 | 1.5888 | 1.5421 | 1.498 | 1.4564 | 1.417 | 1.3797 | 1.3444 | 1.3108 | 1.2788

## Slide 18
Particulars | Units | DHAMPUR SUGAR MILLS LTD, DIST- BIJNOR (U.P.) | 
 |  | B-Heavy | C-Heavy
Capacity | KLPD | 200 | 200
Ethanol Production | Lts | 204851 | 2011052.6
Molasses Consumption | Qtls | 6600 | 90450
Wash Distilled | Lts | 1757250 | 25305000
Wash Made | Lts | 1712167 | 25977000
Molasses TRS | % | 58.91 | 48.11
Fermentable Sugar | % | 55.02 | 43.8
Recovery | Lt/Qtl | 30.96 | 23.8
Fermentation Efficiency | % | 88.47 | 85.9
Distillation Efficiency | % | 98.13 | 98.2
Overall Efficiency | % | 86.81 | 84.9
Alcohol in wash | % | 11.87 | 8.47
Steam Consumption | Kg/Lt | 2.37 | 2.79
Power Consumption | kWH/Lt | 0.15 | 0.16
Spent Wash Generation | % | 6.32 | 9.19
Sugar loss | % | 1.52 | 

## Slide 19
Particulars | Units | SHRI DATTA SAKHAR KARKHANA LTD, A Unit of Dalmia Bharat Sugar and Industries Ltd Kolhapur ( Maharashtra ) | 
 |  | B-Heavy | C-Heavy
Capacity | KLPD | 60 | 60
Ethanol Production | Litre | 55767 | 48118
RS produce | Litre | 3405.78 | -
Molasses Consumption | Qtls | 184.5 | 194.4
Wash Distilled | Lts | 487527 | 441653
Wash Made | Lts | 500292 | 447850
Molasses TRS | % | 59.65 | 48.82
Fermentable Sugar | % | 55.96 | 43.32
Recovery | Lt/Qtl | 32.07 | 24.76
Fermentation Efficiency | % | 90.25 | 89.99
Distillation Efficiency | % | 98.53 | 98.50
Overall Efficiency | % | 88.92 | 88.65
Alcohol in wash | % | 12.31 | 11.05
Steam Consumption | Kg/Lt | 3.87 | 5.21
Power Consumption | kWH/Lt | 0.314 | 0.352
Spent Wash Generation | lts/lts | 6.3 | 6.8
Sugar loss | % | 0.95 | 

## Slide 20: Conclusion
  Diversion of B-Hy molasses for ethanol production may be an attractive preposition at the prevailing sugar prices.
  At the prevailing prices of ethanol produced from B-Hy molasses, even with sugar prices up to around Rs 35/-per kg. It would be advantageous to produce ethanol.
  With B-Hy molasses, there shall be gain in capacity of the distillery, increased in distillation & fermentation efficiencies and reduction in consumption of utilities.
  Diversion of B-Hy molasses may prove to be an effective measure in balancing the demand supply position of sugar.
  Minimum changes are required in the sugar factory and distillery set up except for those required as per guide lines issued by the government of India

## Slide 21: Thanks