## Slide 1
Global Sensory Excellence
Binod Maitin
FlavorActiV Limited, UK
Technical Seminar
New Delhi , February 7-8, 2019
“Assuring Ultrapure Quality of Neutral Alcohol for Vodka & Gin – An Overview”

## Slide 2
Contents
Neutral Alcohol - Quality Imperatives
Off-notes & Specifications
Fermentation & Distillation Imperatives
Monitoring & removal of congeners traces
Effective Analytical Methods
Sensory Evaluation Methods
Sensory Proficiency

## Slide 3
  High-purity potale ethanol ( 96 % ABV ) from agricultural crops
  Base for premium vodka, gin, & several speciality spirits
  Neutral smell and taste and negligible impurities are critical
  Even after multiple distillations traces of congeners remains causing unacceptable odours
Grain Neutral Spirit (GNS) or Extra Neutral Alcohol(ENA)

## Slide 4
Neutral Alcohol Purity is critical
Any off note from impurities/contamination adversely affects
  Product sensory quality
  Aroma & flavour profile,
  Consistency and stability
  Effect on post-consumption well-being ( Taste , Hangover, Toxicity)
Neutral spirits can exhibit objectionable off notes beyond MDL of analytical instruments but fall within sensory threshold of panellists
Structured sensory panellists training and regular proficiency calibration enhances trustworthiness of sensory quality decisions

## Slide 5
Sensory Analysis vs. GC Analysis Data of Vodka

## Slide 7
    Aldehyde Level
      Causes Harshness & raw characters
      Faster oxidation /less Blend Stability
      Contributing to hangover / Carcinogenic
    Methanol Content
      Spirity/solventy/Pungency/ Causes faster oxidation
      Faster Hangover /Toxic at higher level
      Metabolizes by ADH & ALDH to formic acid causing blindness
    N-Propanol Content
      Causes harshness / Faster oxidation at higher level
      Causes depression / Faster Metabolization by ADH & ALDH
    Fusel Oil / Higher Alcohols
      Pungent, Harsher burning sensation
      Different profile, faster oxidation
      Metabolizes slowly by ADH & ALDH
      Contributing to hangover
Consumer Perception & Health Concerns

## Slide 8
Neutral Spirit Specifications for Off - Note Congeners

## Slide 9: Congeners Formation during Fermentation

## Slide 10: No Congeners Desired in Ultrapure Neutral Alcohol
270nm | UV-Visible Spectrophotometric Test Method | abs | - | 0.0000
at 240nm |  | abs | - | 0.030
at 230nm |  | abs | - | 0.079
at 230nm |  |  |  | 
at 220nm |  | abs | - | 0.166
GC Purity
Sensory Neutrality
UV purity

## Slide 11: Critical Fermentations Imperatives
Consistent fermentation
Vitality
Rapidfermentation
Alcohol yield & consistent fermentation yield
Temperature/ Osmotic /Ethanol stress tolerance
Consistent temperature
Controlled pH condition
Competitive against lactic acid bacteria
Reduced yeast biomass producion

## Slide 12: Critical Distillation Imperatives
Separate congeners with boiling points close to ethanol using hydro-selection/extractive distillation.
Demethylising column
Ozonation, activated carbon adsorption and gas stripping
Look at newer ideas : iStill Distilling with carbon extraxtor introduced recently for craft segment

## Slide 13
Next generation alcohol production equipment
Helps the distiller with automated and robotized controls
To make either the best taste rich or neutral spirits
Utilizes carbon in the Extractor to remove congener traces
iStill Distillation With Extractor

## Slide 14
Analytical Detection for monitoring Olfactry-GCMS, Electronic Nose / Tounge
Enhanced Sensory Sensitivity through Good Sensory Practices
Monitoring & removal of Congener traces

## Slide 15
Sensory Evaluation Methods for Neutral Spirits
Scoring (Ratio Scale 0 -10)
Threshold or Sensitivity Tests
Difference Tests
  Triangle & Tetrad
  Difference from Control (DFC)
    An adaptation of Degree of Difference test
    Deals with batch to batch variations.
    Discrimination sensory testing with an identified control evaluate & scale perceived difference from control.
  Category scale from “Not Different” to “Extremely Different”. !

## Slide 16
GMP Flavours Facilitates Retronasal Tasting
The Nose & Mouth are connected. Molecules released into the air inside our mouths as we chew and swallow travel up through the retronasal passage into the nose, then move up and contact the olfactory epithelium. Flavor is the combination of true taste (sweet, salty, sour, bitter) and retronasal olfaction and mouthfeel

## Slide 17: Flavour release and transport in the mouth and nose

## Slide 18
GMP Flavours For Sensory Panel Training and Proficiency Calibration

## Slide 19
Structured approach in developing sensory skills

## Slide 20: Method of Proficiency Assessment?
Measures & Calibrate sensory skills of spirit assessors
Gives a common language of typical off-notes in NS
Ultimately improves quality of the produced NS & NS based spirits beverages

## Slide 21
Proficiency - Taste
Produced to GMP Quality Standards
Colour coded format for easy use
Provided in Pharmaceutical blister packs – protected from air and moisture and easy to use
Documentation and labels provided
Test to results takes 30 mins

## Slide 22
Sensory Proficiency Scheme –
Methods of Validation
Flavour Identification Validation:
Individual flavour identification using standard terminology
Rank Rating Validation:
Discrimination of different flavour intensities and scale them accordingly
In Profile Validation:
Primary focus on IN or OUT / meeting the brand‘s sensory profile – used by spirits customers

## Slide 23
Assuring value from best sensory practices

## Slide 24
Thank You
Questions ?